# i-GLASS™

Guide Specifications for USA and Canada

The specifications below are offered as desirable inclusions in glass and glazing specifications but are not intended to be complete. An appropriate and qualified design professional must verify suitability of a particular product for use in a particular application as well as review final specifications.

# SECTION 08 81 13

DECORATIVE GLASS GLAZING

PART 1 GENERAL

  - SUMMARY

- Section Includes:  Digitally printed glass, including heat-treated, insulating glass units and laminated glass.

- Related Sections

  - Drawings, General and Supplementary Conditions of the Contract, Division 1 and the following Specification Sections, apply to this Section.

  - Section 08 41 00 – Entrances and Storefronts

  - Section 08 42 00 – Entrances

  - Section 08 43 00 – Storefronts

  - Section 08 44 00 – Curtain Wall and Glazed Assemblies

  - Section 08 50 00 – Windows

  - Section 08 60 00 – Roof Windows and Skylights

  - Section 08 81 00 – Glass Glazing

  - REFERENCES

(Note:  Delete all reference standards that are not actually required and add any additional standards required by the municipality and/or state where the project is located.  The Contracting Requirements or Division 1, Section 01420 – References, may establish the edition date of standards not otherwise indicated.  Division 1 may include full names and addresses of the organizations whose standards are referenced.)

- United States

  - ANSI Z97.1 - American National Standard for Glazing Materials Used in Buildings - Safety Performance Specifications and Methods of Test.

  - ASTM C162 - Standard Terminology of Glass and Glass Products.

  - ASTM C724 – Standard Test Method for Acid Resistance of Ceramic Decorations on Architectural-Type Glass.

  - ASTM C1036 - Standard Specification for Flat Glass.

  - ASTM C1048 - Standard Specification for Heat-Treated Flat Glass -- Kind HS, Kind FT Coated and Uncoated Glass.

  - ASTM C1172 - Standard Specification for Laminated Architectural Flat Glass.

  - ASTM C1376 - Standard Specification for Pyrolytic and Vacuum Deposition Coatings on Glass

  - ASTM E1300 - Standard Practice for Determining the Minimum Thickness and Type of Glass Required to Resist a Specified Load.

  - ASTM E2188 - Standard Test Method for Insulating Glass Unit Performance.

  - ASTM E2189 - Standard Test Method for Testing Resistance to Fogging in Insulating Glass Units.

  - ASTM E2190 - Standard Specification for Insulating Glass Unit Performance and Evaluation.

  - CPSC 16 CFR 1201 - Safety Standard for Architectural Glazing Materials.

  - Insulating Glass Manufacturers Alliance (IGMA) - Glazing Guidelines.

- Canada

  - CAN/CGSB-12.1-M - Tempered or Laminated Safety Glass.

  - CAN/CGSB-12.2-M - Flat, Clear Sheet Glass.

  - CAN/CGSB-12.3-M - Flat, Clear Float Glass.

  - CAN/CGSB-12.4-M - Flat, Heat Absorbing Glass.

  - CAN/CGSB-12.8-M - Insulating Glass Units.

  - CAN/CGSB-12.9-M - Spandrel Glass.

  - CAN/CGSB-12.10-M - Light and Heat Reflecting Glass.

  - Insulating Glass Manufacturers Association of Canada (IGMAC) - Glazing Guidelines.

- United States & Canada

  - GANA Glazing Manual; Glass Association of North America.

  - GANA Sealant Manual; Glass Association of North America.

  - GANA Laminated Glass Design Guide; Glass Association of North America.

  - GANA/GTA 66-9-20 - Specification for Heat-Strengthened or Fully Tempered Ceramic Enameled Spandrel Glass for Use in Building Window/Curtain Walls and Other Architectural Applications.

  - GANA/GTA 89-1-6 - Specification for Environmental Durability of Fully Tempered or Heat-Strengthened Spandrel Glass with Applied Opacifiers.

  - GANA/GTA 95-1-31 - Specification for Decorative Architectural Flat Glass.

  - Oldcastle BuildingEnvelope® - Glazing Instructions.

  - DEFINITIONS

- Sealed Insulating Glass Unit Surfaces & Coating Orientation:

- Surface 1 – Exterior surface of outer pane (surface facing outdoors of outboard lite).

- Surface 2 – Interior surface of outer pane (surface facing indoors of outboard lite).

- Surface 3 – Exterior surface of inner pane (surface facing outdoors of inboard lite).

- Surface 4 – Room side surface of inner pane (surfacing facing indoors of inboard lite).

  - SYSTEM DESCRIPTION

- Design Requirements

- Provide glazing systems capable of withstanding normal thermal movements, windloads and impact loads, without failure, including loss due to defective manufacture, fabrication and installation; deterioration of glazing materials; and other defects in construction.

- Provide glass products in the thicknesses and strengths (annealed or heat-treated) required to meet or exceed the following criteria based on project loads and in-service conditions per ASTM E1300.

  - Minimum thickness of annealed or heat-treated glass products is selected, so the worst-case probability of failure does not exceed the following:

    - 8 breaks per 1000 for glass installed vertically or not over 15 degrees from the vertical plane and under wind action.

    - 1 break per 1000 for glass installed 15 degrees or more from the vertical plane and under action of wind and/or snow.

  - SUBMITTALS

- Submit 12-inch (305mm) square samples of each type of glass indicated (except clear monolithic glass products), and 12-inch (305mm) long samples of each color required (except black) for each type of sealant or gasket exposed to view.

- Submit manufacturer’s product data sheet and glazing instructions.

- Glazing contractor shall obtain compatibility and adhesion test reports from sealant manufacturer, indicating that glazing materials were tested for compatibility and adhesion with glazing sealant, as well as other glazing materials including insulating units.

- Glazing Contractor shall provide test reports showing that the glass meets the requirements of any security test reports specified on drawings.

  - QUALITY ASSURANCE

- Comply with published recommendations of glass product manufacturers and organizations below, except where more stringent requirements are indicated. Refer to these publications for glazing terms not otherwise defined in this section or referenced standards.

- GANA Publications

- AAMA Publications

- IGMA/IGMAC Publications

- Safety glass products in the US are to comply with CPSC 16 CFR Part 1201 for Category II materials.

- Safety glass products in Canada are to comply with the testing requirements of CAN/CGSB-12.1-M, Type 1 for Laminated Glass and Type 2 for Tempered Glass.

- Provide safety glass permanently marked with the company name or logo and CAN/CGSB-12.1-M if the product meets categories 1 and 2, or mark as CAN/CGSB 12.1-M-1 if the product meets the requirements of Category 1 only.

- Insulating Glass products are to be permanently marked either on spacers or at least one insulating unit component with appropriate certification label of inspecting and testing agency indicated below:

- US - Insulating Glass Certification Council (IGCC)

- Canada - Insulating Glass Manufacturers Alliance (IGMA) or Insulating Glass Manufacturers Association of Canada (IGMAC)

- Single-source fabrication responsibility: All glass fabricated for each type shall be processed and supplied by a single fabricator.

  - DELIVERY, STORAGE AND HANDLING

- Comply with manufacturer’s instruction for receiving, handling, storing and protecting glass & glazing materials.

- Delivery: Deliver materials in manufacturer’s original, unopened, undamaged containers with identification labels intact.

- Storage and Protection: Store materials protected from exposure to harmful environmental conditions and at temperature and humidity conditions recommended by the manufacturer.

- Exercise exceptional care to prevent edge damage to glass, and damage/deterioration to coating on glass.

- Where insulating glass units will be exposed to substantial altitude changes, comply with insulating glass fabricator’s recommendations of venting and sealing.

  - PROJECT / SITE CONDITIONS

- Environmental Requirements: Installation of glass products at ambient air temperature below 40 degrees F (4.4 degrees C) is prohibited.

- Field Measurements: When construction schedule permits, verify field measurements with drawing dimensions prior to fabrication of glass products.

  - WARRANTY

- Provide a written 10-year limited warranty from date of manufacture for insulating glass. Warranty covers deterioration due to normal conditions of use and not to handling, installing, protecting and maintaining practices contrary to glass manufacturer’s published instructions.

- Provide a written minimum 10-year warranty from date of manufacture for digitally printed ceramic frit decorative glass.  Warranty covers deterioration due to normal conditions of use and not to handling installing, protecting and maintaining practices contrary to glass manufacturer’s published instructions.

- Provide written 10-year warranty from date of manufacture for laminated glass. Warranty covers deterioration due to normal conditions of use and not to handling installing, protecting and maintaining practices contrary to glass manufacturer’s published instructions.

- Provide a written warranty from date of manufacture for tempered glass.

- Provide a written 10-year limited warranty from date of manufacture for all coated products.

PART 2 PRODUCTS

  - MANUFACTURERS

- Manufacturer is used in this section to refer to a firm that produces primary glass or fabricated glass as defined in the referenced standards.

  - Oldcastle BuildingEnvelope®

  - Guardian Industries

  - Pilkington

  - Vitro Architectural Glass (formerly PPG)

  - MATERIALS

- Decorative Monolithic Float Glass

- Glass Type: Oldcastle BuildingEnvelope® i-Glass™

- Glass Tint:

- Nominal Thickness:

- Glass Strength: (Heat-Strengthened, Tempered)

- Coating Orientation: Surface #2

- Ceramic Ink: Dip-Tech Spectrum™ Inks

- Digital Image File Name:

- ASTM C724 Requirements:

  - Hydrochloric acid 2-3 (3.7% HCl, 5 min, 22°C)

  - Acetic acid 1-2 (4% acetic acid, 15 min, 22°C)

  - Citric acid 1-2 (10% citric acid, 15 min)

  - Sulfuric acid 4 hr (0,1N H2SO4, 80°C, no change in color on glass side)

  - Alkali resistance 1-2 (0,1N NaOH, 15 min, 22°C)

- US Requirements:

  - Heat-Strengthened float glass shall comply with ASTM C1048, Type I, Class 1 (clear), Class 2 (tinted), Quality Q3, Kind HS.

  - Tempered float glass shall comply with ASTM C1048, Type I, Class 1 (clear), Class 2 (tinted), Quality Q3, Kind FT.

- Canadian Requirements:

  - Heat-Strengthened float glass shall comply with CAN/CGSB-12.9-M, Type 2-Heat-Strengthened, Class A-Float Glass.

  - Tempered float glass shall comply with CAN/CGSB-12.1-M, Type 2, Tempered Glass, Class B-Float Glass.

- Glass shall be heat-strengthened or tempered as required by codes, or as required to meet thermal stress and wind loads.

- Glass heat-treated by horizontal (roller hearth) process with inherent roller wave distortion parallel to the bottom edge of the glass as installed when specified.

- Decorative Sealed Insulating Glass (IG) Units with i-Glass™ Outboard Lite

- Insulating Glass Unit Makeup

- Outboard Lite

  - Glass Type: Oldcastle BuildingEnvelope® i-Glass™

  - Glass Tint:

  - Nominal Thickness:

  - Glass Strength: (Heat-Strengthened, Tempered)

  - Coating Orientation: Surface #2

  - Ceramic Ink: Dip-Tech Spectrum™ Inks

  - Digital Image File Name:

  - ASTM C724 Requirements:

    - Hydrochloric acid 2-3 (3.7% HCl, 5 min, 22°C)

    - Acetic acid 1-2 (4% acetic acid, 15 min, 22°C)

    - Citric acid 1-2 (10% citric acid, 15 min)

    - Sulfuric acid 4 hr (0,1N H2SO4, 80°C, no change in color on glass side)

    - Alkali resistance 1-2 (0,1N NaOH, 15 min, 22°C)

- Spacer

  - Nominal Thickness:

  - Gas Fill: (Air or 90% Argon)

- Inboard Lite

  - Glass Type:

  - Glass Tint:

  - Nominal Thickness:

  - Glass Strength: (Annealed, Heat-Strengthened, Tempered)

  - Coating Orientation: (N/A, Surface #___)

- Provide hermetically sealed IG units with dehydrated airspace, dual sealed with a primary seal of polyisobutylene (PIB) and a secondary seal of silicone or an organic sealant depending on the application.

- US Requirements:

  - Insulating glass units are certified through the Insulating Glass Certification Council (IGCC) to ASTM E2190.

- Canadian Requirements:

  - Insulating glass units are certified through the Insulating Glass Manufacturers Association of Canada (IGMAC) to CAN/CGSB-12.8, or to the Insulating Glass Manufacturers Alliance (IGMA) Certification Program for ASTM E2190.

- Decorative Sealed Insulating Glass (IG) Units with i-Glass™ Inboard Lite

  - Insulating Glass Unit Makeup

    - Outboard Lite

      - Glass Type:

      - Glass Tint:

      - Nominal Thickness:

      - Glass Strength: (Annealed, Heat-Strengthened, Tempered)

      - Coating Orientation: (N/A, Surface #___)

    - Spacer

      - Nominal Thickness:

      - Gas Fill: (Air or 90% Argon)

    - Inboard Lite

      - Glass Type: Oldcastle BuildingEnvelope® i-Glass™

      - Glass Tint:

      - Nominal Thickness:

      - Glass Strength: (Heat-Strengthened, Tempered)

      - Coating Orientation: Surface #3

      - Ceramic Ink: Dip-Tech Spectrum™ Inks

      - Digital Image File Name:

      - ASTM C724 Requirements:

        - Hydrochloric acid 2-3 (3.7% HCl, 5 min, 22°C)

        - Acetic acid 1-2 (4% acetic acid, 15 min, 22°C)

        - Citric acid 1-2 (10% citric acid, 15 min)

        - Sulfuric acid 4 hr (0,1N H2SO4, 80°C, no change in color on glass side)

        - Alkali resistance 1-2 (0,1N NaOH, 15 min, 22°C)

  - Provide hermetically sealed IG units with dehydrated airspace, dual sealed with a primary seal of polyisobutylene (PIB) and a secondary seal of silicone or an organic sealant depending on the application.

  - US Requirements:

    - Insulating glass units are certified through the Insulating Glass Certification Council (IGCC) to ASTM E2190.

  - Canadian Requirements:

    - Insulating glass units are certified through the Insulating Glass Manufacturers Association of Canada (IGMAC) to CAN/CGSB-12.8, or to the Insulating Glass Manufacturers Alliance (IGMA) Certification Program for ASTM E2190.

- Decorative Monolithic Two-Ply Laminated Glass*

- Laminated Glass Makeup

- Outer Ply

- Glass Type: Oldcastle BuildingEnvelope® i-Glass™

- Glass Tint:

- Nominal Thickness:

- Glass Strength: (Heat-Strengthened, Tempered)

- Coating Orientation: Surface #2

- Ceramic Ink: Dip-Tech Spectrum™ Inks

- Digital Image File Name:

- ASTM C724 Requirements:

  - Hydrochloric acid 2-3 (3.7% HCl, 5 min, 22°C)

  - Acetic acid 1-2 (4% acetic acid, 15 min, 22°C)

  - Citric acid 1-2 (10% citric acid, 15 min)

  - Sulfuric acid 4 hr (0,1N H2SO4, 80°C, no change in color on glass side)

  - Alkali resistance 1-2 (0,1N NaOH, 15 min, 22°C)

- Interlayer

- Interlayer Type:

- Interlayer Tint:

- Nominal Thickness:

- Inner Ply

- Glass Type:

- Glass Tint:

- Nominal Thickness:

- Glass Strength: (Heat-Strengthened, Tempered)

- Coating Orientation: (N/A, Surface #___)

- Laminated glass products to be fabricated in autoclave with heat, plus pressure, free of foreign substances and air pockets.

- Interlayer material: Polyvinyl Butyral or Ionoplast sheets.

- US Requirements:

  - Laminated glass shall comply with ASTM C1172 and with other requirements as specified.

- Canadian Requirements:

  - Laminated glass shall comply with CAN/CGSB-12.1-M, Type 1-Laminated Glass, Class B-Float Glass and with other requirements as specified.

- Glazing Products

- Select appropriate glazing sealants, tapes, gaskets and other glazing materials of proven compatibility with other materials that they contact. These include glass products, insulating glass unit seals and glazing channel substrates under installation and service conditions, as demonstrated by testing and field experience.

PART 3 EXECUTION

  - EXAMINATION

- Site Verification and Conditions

- Verify that site conditions are acceptable for installation of the glass.

- Verify openings for glazing are correctly sized and within tolerance.

- Verify that a functioning weep system is present.

- Verify that the minimum required face and edge clearances are being followed.

- Do not proceed with glazing until unsatisfactory conditions have been corrected.

  - PREPARATION

  - Protection

- Handle and store product according to manufacturers’ recommendations.

  - Surface Preparation

- Clean and prepare glazing channels and other framing members to receive glass.

- Remove coatings and other harmful materials that will prevent glass and glazing installation required to comply with performance criteria specified.

  - INSTALLATION

- Install products using the recommendations of manufacturers of glass, sealants, gaskets and other glazing materials, except where more stringent requirements are indicated, including those in the “GANA Glazing Manual”.

- Verify that Insulating Glass (IG) Unit secondary seal is compatible with glazing sealants.

- Install glass in prepared glazing channels and other framing members.

- Install setting blocks in rabbets as recommended by referenced glazing standards in GANA Glazing Manual and IGMA Glazing Guidelines.

- Provide bite on glass, minimum edge and face clearances and glazing material tolerances recommended by GANA Glazing Manual.

- Provide weep system as recommended by GANA Glazing Manual.

- Set glass lites in each series with uniform pattern, draw, bow and similar characteristics.

- Distribute the weight of the glass unit along the edge rather than at the corner.

- Comply with manufacturer’s and referenced industry recommendations on expansion joints and anchors, accommodating thermal movement, glass openings, use of setting blocks, edge, face and bite clearances, use of glass spacers, edge blocks and installation of weep systems.

- Protect glass from edge damage during handling and installation.

- Prevent glass from contact with contaminating substances that result from construction operations, such as weld spatter, fireproofing or plaster.

- Remove and replace glass that is broken, chipped, cracked or damaged in any way.

  - CLEANING

- Clean excess sealant or compound from glass and framing members immediately after application, using solvents or cleaners recommended by manufacturers.

- Glass to be cleaned according to:

- GANA Glass Informational Bulletin GANA 01-0300 - Proper Procedures for Cleaning Architectural Glass Products.

- GANA Glass Information Bulletin GANA TD-02-0402 – Heat-Treated Glass Surfaces Are Different.

- Do not use scrapers or other metal tools to clean glass.

END OF SECTION